## Slide 1: SafeDrive: Online Driving Anomaly Detection From Large-Scale Vehicle Data
ECE 693 Big Data Security

## Slide 2: Big Picture
Identifying driving anomalies is of great significance for improving driving safety. The development of the Internet-of-Vehicle (IoV) technology has made it feasible to acquire big data from multiple vehicle sensors, and such big data play a fundamental role in identifying driving anomalies.
Existing approaches are mainly based on either rules or supervised learning. However, such approaches often require labeled data, which are typically not available in big data scenarios.
In addition, because driving behaviors differ under vehicle statuses (e.g., speed and gear position), to precisely model driving behaviors needs to fuse multiple sources of sensor data.
To address these issues, in this paper, we propose SafeDrive, an online and status-aware approach, which does not require labeled data. From a historical dataset, SafeDrive statistically offline derives a state graph (SG) as a behavior model. Then, SafeDrive splits the online data stream into segments and compares each segment with the SG.
SafeDrive identifies a segment that significantly deviates from the SG as an anomaly. We evaluate SafeDrive on a cloud-based IoV platform with over 29 000 real connected vehicles.

## Slide 3: Why this research?
the prior research cannot effectively identify abnormal driving behaviors for three main reasons.
First, in IoV, the volume of data is huge. They are collected from multiple sensors and are with complicated relations, making it infeasible to label normal and abnormal behaviors.
Second, the process of manually labeling the huge volume of the data stream can be difficult and biased because abnormal driving behaviors can be uncertain and human perceptions can be error-prone.
Third, whether a driving behavior is abnormal or not is heavily dependent on the current vehicle status (e.g., speed and gear position).
For instance, Fig. 1 shows the relationship between acceleration behaviors and vehicle speed statuses. It can be observed that drivers would normally accelerate more slowly when driving at high speed. Such behavior is a kind of (1) contextual-status-related behaviors.
As a comparison, another behavior can be observed in the relations between different types of data, and such behavior is a kind of (2) correlational-status-related behaviors.

## Slide 5: Big picture of SafeDrive
We propose SafeDrive, an online and status-aware approach for detecting driving anomalies.
SafeDrive does not require costly labeled data, by employing a state graph (SG). SafeDrive fuses data on both the vehicle sensor level and the fleet level; such data precisely reflect the normal driving styles.
For the online detection, SafeDrive compares the real-time driving data stream with the SG to detect anomalies.
SafeDrive includes novel techniques to address two main challenges:
uniformly modeling a variety of vehicle statuses represented by complex data relations; and
capturing how people normally drive based on the modeled relations between statuses.

## Slide 6: It uses graph
In particular, SafeDrive includes an SG to model 1) contextual relations between statuses of the same type of data, such as speed, at different timings and 2) correlational relations between statuses of different types of data, such as the vehicle revolutions per minute (RPM) and gear position, at the same timing.
SafeDrive represents all the statuses as states and connected with edges in the graph. To construct an objective driving model, SafeDrive fuses different vehicles’ historical data together and statistically calculates the structure of the SG. In the online setting, SafeDrive identifies driving anomalies by splitting the data stream into segments and comparing each segment with the SG.
SafeDrive considers as abnormal those segments that largely deviate from the SG.
We implement SafeDrive on a real-world cloud-based IoV platform, which connects over 29,000 vehicles from 60 cities. Each vehicle is equipped with an on-board diagnostics (OBD) connector to collect the vehicle’s parameter values and send the data to the server through the mobile wireless network.

## Slide 8: Module A. Offline Building of a Driving Behavioral Model
Our basic idea is to uniformly model the status relations of streamed vehicle data in a weighted SG, in which the state is a term used to represent the value (or its range) of data attributes. Specifically, we adopt discrete states to quantify status (data values) and employ weighted edges (connections between states) to measure the relationship between states.
The states are generated from different sensor data and connected with each other via weighted edges, in which manner the model can combine multiple data, even those with different frequencies.
The structure of the graph is constructed based on statistics of the historical data; as a result, the graph becomes a detailed behavioral model for fusing different vehicle data.
In this way, the graph structure can objectively reflect how people usually drive under different conditions or statuses since the weights are generated from real-world data. The formal definition of an SG is given in Definition 1.
Definition 1 (SG): An SG =< S,E >is a weighted directed graph, where S is a set of states and E is a set of weighted edges. A weighted edge e ∈ E corresponds to a kind of relation between states, where weight w ∈ (0, 1].

## Slide 9: Module B. Online Anomaly Detection
In many cloud-based applications, the collected driving data are often organized as a stream or data sequence where each data instance contains different attributes.
The stream, as stated earlier, reflects driving behaviors (related to contextual and correlational statuses) where anomalies may occur.
To detect anomalies online, we first split the newly arrived data instances in data stream into segments and then map each segment as a Temporal Subgraph (TS-SG), which is further evaluated by being compared with the offline-generated SG model.
The subgraph (or segment) that significantly deviates from the SG model is considered as an anomaly. The formal definition of a temporal subgraph is given in Definition 2.

## Slide 10: States
Formally, in SafeDrive, a state s ∈ S represents a category or a set of data instances. For numerical data, states can be acquired by discretization, while for categorical data, the category itself can be used as a state. In our evaluation (described in Section V), for example, the vehicle speed is generated into 100 states, each of which covers a speed range of ±1 km/h. Acceleration and deceleration behaviors can be reflected by the transitions between those speed states.
Therefore, the abnormal level of acceleration behaviors can be evaluated by the connection weight from speed states with a smaller value to states with higher values. We regard the edge between the same type of states as the contextual edge, which models the contextual driving behaviors reflected by the same kind of OBD data parameters.
Note that for numerical data attributes, a potential risk of discretization is state explosion: a huge number of states might be generated and thus cause an extremely large graph. However, in most of the real world cases, only a limited scope of ranges or data sources are used in practice, largely limiting the scale of the graph.

## Slide 11: Correlated graph
In SafeDrive, different parameters are separately generated into different types of states.
The co-occurrence relations between different types of data reflect the correlational-state-related behaviors. For instance, the speed has a correlation with RPM, e.g., a high RPM value usually implies high vehicle speed.
To strengthen the expression ability of SafeDrive, we use correlational weighted edges to represent the co-occurrence relationships between different types of states. As a result, two kinds of edges are enclosed in the SG, i.e., contextual edges and correlational edges.
Fig. 3 (next slide) illustrates an abstract example of a SG with two types of states, Sa and Sb . Note that in SafeDrive, the SG may contain cycles since the data in a stream can be repeatable.

## Slide 12
Fig. 3. Example of an SG, in which bidirectional arrows represent correlational
edges and unidirectional arrows represent contextual edges.

## Slide 13: Weights for contextual relationship
As discussed earlier, the SG behavioral model is built by two steps: state generation and graph construction.
The first step uses discretization to transfer data ranges of OBD parameters into states, while the second step scans the historical dataset statistically, from which the edges between states and their weights are derived and calculated.
The value of the weight of a contextual edge is computed by below, where t is a time stamp referring to the relative temporal relationship between states. The value of connection weight denotes the conditional probability of s2 appearing at time (t + 1) when s1 appears at t

## Slide 14: Weights for correlational relationship
For a correlational relationship between two different types of states sa and sb , with the objective of presenting a detailed reflection of the correlation, we implement it with two conditional edges separately, i.e., from sa to sb and from sb to sa .
Their weights can be calculated according to the equation (2) below. As can been seen in (2), the values of connection weights denote the probability of sb appearing at time t given the condition of sa appears at t, and the probability of sa appearing at time t given the condition of sb appears at t. Note that the correlational edges between sa and sb are asymmetric since w(sa, sb ) is usually not equal to w(sb, sa )
Bi-directional (correlational edges)
Weights are probabilities

## Slide 15: ONLINE ABNORMAL DETECTION WITH SafeDrive
Typically, we evaluate driving behaviors for each short period of time. To that end, after the SG is built, we use it to measure the online stream data.
The data stream is split into segments, each of which is a behavior unit and being mapped to a TS-SG. The segmentation length is based on the time duration for completing a behavior. Our empirical investigation suggests that an interval of 10–15 s is suitable to represent a driving behavior.
Unlike other subgraphs, a TS-SG contains contextual information of data stream. In such a graph, a state is allowed to appear repeatedly given that specific data are likely to be generated repeatedly. For example, when driving in a stable status, many of the sampled speed data in the uploading stream might be the same; hence, the TS-SG may contain some recurring states with different time stamps.
The states of TS-SG are generated in the same way that the states of the SG are generated. The edges in TS-SG also have weight values assigned according to their counterpart edges in the original SG. (TS-SG is just a subgraph of SG anyway). For example, if there is an edge from sa to sb in a TS-SG, then its weight value equals to the value of w(sb, sa ) in the SG. Specifically, if no such edge exists in the SG, the graph would be updated by SafeDrive automatically.

## Slide 16: Anomaly score
After the TS-SG of each segment is generated, according to (3) below, we compute an anomaly score for the subgraph TS-SG, marked as f(TS-SG).
Given that the aim of the score is to filter out those state connections with low probabilities, we hereby employ an inverse proportional function to construct f(TS-SG).
In this manner, we are able to “amplify” low probabilities and filter them out. Note that m is the number of edges in the subgraph.
Basically, we consider the TS-SG with low-probability edges, which usually cause a high value of f(TS-SG), as an anomaly.
The score is compared with δ, a threshold defined manually. If f(TS-SG) > δ, then the subgraph is marked as an anomaly. In practice, it is suggested to choose the threshold δ according to the distribution of score f(TS-SG).
Bigger value means lower prob -> abnormal

## Slide 17: Deduce the driver’s behaviors from graph analysis
Fig. 4 (next slide) shows two abstract examples of the subgraph with different types of anomalies caused by contextual and correlational relationships, respectively. In real-world driving scenarios, contextual and correlational driving anomalies may occur simultaneously because the data are generated by vehicle components closely working together, and a specific abnormal driving behavior or operation may cause various anomalies.
By analyzing the structure of the abnormal TS-SG and evaluating which kind of edge causes a high score value, data analysts are able to understand the detailed reason for this anomaly. For example, if the cause of high f(TS-SG) is vehicle-speed state transition, it signifies that the driver behaves not so well in accelerating or decelerating.
While if RPM states cause the high score, it signifies that the driver does not take a smooth control of accelerator pedal or gear position, suggesting that the driver drives either aggressively or unskillfully.

## Slide 19: Graph evolution
Note that due to the limitation of historical data, change of environment, or people’s driving styles, the structure of the graph may need to be able to evolve over time. Such a characteristic is known as concept drift in anomaly detection for streaming data [18]. In this scenario, for example, given two states, si and sj , when measured in different times, w(si, sj ) could be different.
As a result, the abnormal level of sequence si, sj changes over time. Failing to sense or account for such change could lower the performance of the detector by causing many false alarms.
We address this problem by designing a module in the cloud named SG-Maintainer to maintain and update the SG. In practice, the SG-Maintainer maintains an array that records the connection number between states.
It updates the array when each data arrives and then periodically calculates the connection weights of the SG according to the array. Given a data sequence DS, the online detection is described in Algorithm 1.

## Slide 21: Evaluation

## Slide 23
Contextual: the same variable; different times (only look at ONE curve)

## Slide 24
Look at two curves; their relationship in the same time.