## Slide 1: Comprehensive Experimental Analyses of Automotive Attack Surfaces
Stephen Checkoway, Damon McCoy, Brian Kantor, Danny Anderson, Hovav Shacham, and Stefan Savage
University of California, San Diego
Karl Koscher, Alexei Czeskis, Franziska Roesner, and Tadayoshi Kohno
University of Washington
Presented by
Tejaswee Bhargava Pasumarti

## Slide 2: Authors
Stephen Checkoway
Research interests are in (embedded) systems security, health IT security, and voting particularly in voting security and post-election auditing.
Damon McCoy
Research includes work on wireless privacy, anonymous communication systems, cyber-physical security, and economics of e-crime.
Brian Kantor
Research interests include: Wireless and satellite communications, digital signal processing
Alexei Czeskis
Authentication in a variety of contexts: from resource constrained embedded devices (for example in RFIDs or automotive systems) to online transactions involving powerful desktop computers, and, of course, mobile devices.
Franziska Roesner
Research interests: security, privacy and systems.
Karl Koscher
Analyzing how information can leak from deniable file systems, developing embedded systems.
Hovav Shacham
Cybersecurity Policy, cryptography

## Slide 3: Abstract
Modern automobiles are pervasively computerized.
Vulnerable to attacks.
Internal networks within modern cars are insecure.
Whether automobiles are susceptible to remote compromise.
Broad range of attack vectors.
Wireless communications channels usage.
Structural characteristics of automotive system and practical challenges.

## Slide 4: Outline
Introduction
Threat Model
Vehicle Attack Service
Vulnerability Analysis
Indirect Physical Exploits
Short-range Wireless Exploits
Long-range Wireless Exploits
Threat Motivation
Fixes & Conclusion

## Slide 5: Introduction
Modern cars controlled by complex distributed computing systems.
Systems are controlled by tens of heterogeneous processors (ECUs)
    ECUs : is a controller with responsibilities including braking, lighting, gps etc
    Each ECU has multiple interfaces fro different buses
Millions of lines of code
Multiple separate communication buses
Benefits like efficiency, safety, cost
New attacks are possible
Analysis of external attack vectors

## Slide 6: Threat Model
Technical Capabilities
  Capabilities in analyzing the system and developing exploits
  Focuses on making technical capabilities realistic
Operational capabilities
  Analysis of attack surface of vehicles
  How malicious payload is delivered
  Indirect physical access, short-range wireless, long-range wireless accesses

## Slide 7: Vehicle attack surface
Indirect physical access
OBD-II
  On board diagnostics II
  Connects to all key CAN buses of vehicle
  Used during vehicle maintenance
Entertainment : Disc, USB, iPod

## Slide 8: Vehicle attack surface
Short-range wireless access
Bluetooth
Remote Keyless Entry
Tire Pressure (TPMS)
Wifi

## Slide 9: Vehicle attack surface
Long-range wireless access
GPS
Satellite radio
Digital radio
Remote Telematics Systems

## Slide 10: Vehicle attack surface

## Slide 11: Vulnerability Analysis
Focused on moderately priced sedan with standard options and components
Cars < 30 ECUS comprising both critical drivetrain components & less critical components
PassThru for ECU diagnosis and reprogramming
Every vulnerability demonstrated allowed complete control of vehicle’s system
  General Procedure:
    Identify microprocessor (PowerPC, ARM, Super-H, etc)
    Extract firmware and reverse engineer using debugging devices/software where possible
    Exploit vulnerability or simply reprogram ECU

## Slide 12: Exploitation Summary

## Slide 13: Indirect physical exploits
Media Player
Accepts compact discs
Software running on CPU handles audio parsing, UI functions, handles connections
Two exploits
  Latent update capability of player manufacturer
      Updates when user does nothing
  WMA parser vulnerability
      Audio file parse correctly on a PC - In vehicle send arbitrary CAN packets

## Slide 14: Indirect physical exploits
OBD-II
Looked at PassThru device from manufacturere
Found no authentication for PC’s on same WiFi network
Found exploit allowing reprogramming of PassThru
  Allows for PassThru worm
  Allows for control of vehicle reprogramming
  Includes unsecured and unused Linux programs

## Slide 15: Short-range wireless exploitation
Bluetooth:
  Found popular Bluetooth protocol stack with custom manufacture code on top
      Custom code contained 20 unsafe calls to strcpy()
  Indirect attack  assumes attacker has paired device
      Implemented Trojan on Android device to compromise machine
  Direct attack  exploits with a paired device
      Requires brute force of PIN to pair device (10 hours)  Limited by response of vehicle’s Bluetooth

## Slide 16: Long-range wireless exploitation
Cellular attack
Telematics
SSL
PPP
3G
Telematics
Software modem
Voice channel
Cell phone

## Slide 17: Long-range wireless exploitation
Telematics Connectivity:
  Similar to Bluetooth  3rd party device with manufacturer code on top
    Again found exploit in transition from 3rd party to manufacturer “Command” program for data transfer
    Lucky for manufacturer  bandwidth did not allow exploit transfer within timeout
      Exploit required of authentication code
        Random nonce not so random
        Bug that allows authentication without correct response

## Slide 18: Threat motivation
Theft:
  Scary version  mass attack cellular network creating vehicle botnet
      Able to have cars report VIN and GPS
      Can unlock doors, start engine and fully startup car
      Cannot disable steering column lock
Surveillance:
  Allows audio recording from in-cabin microphone

## Slide 19: Security fixes
Looked at easily available fixes to exploits:
  Standard security engineering best-practices e.g. don’t use unsafe strcpy  instead strncpy
  Removing debugging and error symbols
  Use stack cookies and ASLR
  Remove unused services e.g. telnet and ftp
  Code guards
  Authentication before re-flashing

## Slide 20: Conclusion
Vulnerability causes:
    Lack of adversarial pressure
    Conflicting interests of ECU software manufacturers and car manufacturers
        Ex: Telematics, Bluetooth & Media Player
        Penetration testing