## Slide 1: Neighborhood Watch: Security and Privacy Analysis of Automatic Meter Reading Systems
Ishtiaq Rouf, Hossen Mustafa
Rob Miller
Marco Grutese
Presented By Krishna Rawali Puppala

## Slide 2: What is a Smart Meter??

## Slide 3: Benefits of having a Smart Meter
No more manual readings.
More accurate bills.
Improves efficiency and reliability.
Real time reports.
And many more.....
But is it SECURE ????

## Slide 4: Beware!! Smart Meters are tracking us

## Slide 5: Recent Articles

## Slide 6: Architecture
  AMR Meters
  Has metering engine &
  ERT(Encoder-Re
  -ceiver-Transmitter)
  AMR Readers
    Handheld devices
    Mobile collectors
    Fixed Network AMR
    - No manual walk.

## Slide 7: Communication Protocol
Meters use simple modulation schemes-
  OOK ( on-off Keying) or FSK ( Frequency Shift Keying) included with the Manchestor Encoding Scheme.
Two types of Communication models-
Wake-up Model
Two-way communication
Reader sends an Activation signal to wake-up the meter.
Bubble-up Model
One-way communication
There is a meter reading broadcast for every 30s.

## Slide 8: Reverse Engineering to discover meter protocol
First step is to capture few transmissions from each meter.
Built a detection software to capture, replay and verify signals.

## Slide 9: AMR Transmission Packets
Pilot Packet-
A high priority control packet associated with the data packet.

## Slide 10: Reverse Engineering to discover meter protocol (cont)
Decoding Packets

## Slide 12: Lessons Learned
Reverse Engineering requires modest effort.
- Anyone can reverse engineer with low cost and effort.
No Encryption.
- Anyone can eavesdrop on real time consumption packets.
Battery drain attacks.
- Wake-up meters transmit a packet as soon as they receive an activation signal.

## Slide 13: Packet Spoofing
Spoofing a packet has become easier.
Packet is spoofed with an arbitrary meter ID and reading.
Observations-
No Authentication.
No Input Validation.

## Slide 15: Neighborhood Monitoring
Eavesdropping Range-
  Tested two locations in a state: Rural and Urban
  Location Range
  Rural 150m
  Urban 70m
  Results- Attacker can able to sniff packets in any area without entering private property.

## Slide 16: Neighborhood Monitoring(cont)
Boosted Eavesdropping Range
How to boost the range at low cost?
- Adding LNA ( Low Noise Amplifier).
- LNA amplifies received signal strength.
Increases eavesdropping range in the urban area from 70m to 300m

## Slide 18: Neighborhood Monitoring
Number of Observed Meters
Used two RF Sniffers –
- Narrowband Sniffer 4 MHz
- Wideband Sniffer 12.5MHz
Meter w/o LNA w LNA
Narrowband 72 161
Wideband 106 485

## Slide 19: Neigborhood Monitoring
Packet Reception Rate
  Received packets per hour (pph)
  Larger pph maps to more frequent energy consumption and high level of information leakage.

## Slide 20
Even at a low packet reception rate, it is very easy to infer data of the residents.

## Slide 21: Inferring Household Events
Visual Observation Mechanisms
- on-board LCD display
- infrared (IR) LED using cameras or IR photodiodes.

## Slide 22: Inferring Household Events
Automated LCD Screen Monitoring
For every consumption of Wh( Watt-hour), one of the dot toggles
Tracks the toggles on a laptop and generates electricity trace.

## Slide 23: Inferring Household Evemts
Infrared LED Monitoring
  For every consumption of 1Wh, IR LED flashes.
  Designed IR circuit to capture the IR flashes.
  Once the diode detects the flash, the voltage becomes high.

## Slide 24: Experiments & Results
  Examined whether RF Sniffing can reveal sensitive information.
  Found that RF sniffing suffered from low granularity of data.
  Question: RF eavesdropping information sufficient to infer sensitive data?
  Ans: Conducted two experiments and found that both camera and IR based methods captured data with high granularity than RF Eavesdropping.

## Slide 25: Results

## Slide 26: Defense Strategies
Spoofing Defenses for Legacy Meters
  Radio fingerprinting techniques.
  Anomaly Detection.
Cryptographic Mechanisms
  Encrypting data packets using standard block encryption algorithms.
  Requires upgrading of the meters.
Jammer add-on
  add-on device PPJ (Privacy Preserving Jammer). No upgradation.

## Slide 27: Privacy Preserving Jammer
Deactivation Protocol

## Slide 28: Conclusion
AMR systems are vulnerable to spoofing attacks.
Continuous broadcast of readings for every 30s risking millions of meters.
Offered a security solution that the authors call PPJ.
  No modification of current meters.
  Prevents information leakage.